## Slide 1: 2019 Trane Latin America Sales Conference

## Slide 3: Portfolio de Productos No UL
3
Serie-Y
Generacion “K” Non-UL
Bomba de Calor
Hasta 563MBH (47 Toneladas)
Hasta 50 unidades interiores
Distancia Max. de90 mts de primera derivacion
Coneccion de unidades interiores hasta 130%
Largo de tuberia total = 1000 mts
Diferencia de elevacion entre unidades interiores= 30 mts
Max. EER = 14.7
Serie-S
Generacion “K” Non-UL
Bomba de Calor
3.5, 4 y 4.5 Toneladas
Hasta 12 unidades interiores
Distancia Max. de90 mts de primera derivacion
Coneccion de unidades interiores hasta 130%
Largo de tuberia total= 300 mts
Diferencia de elevacion entre unidades interiores= 15 mts
Max. EER = 15.28

## Slide 4: Portfolio de Productos UL
4
4
Serie-R2 – “K” “L”
Recobro Energetico – 2 tuberias
Hasta 336MBH (28 Toneladas)
Hasta 50 unidades interiores
Max. 110 mts from ODU to first BC
Max. 60 mts from BC to UI
Combination IUs up to 150% (200%)
Max. pipe length = 937 mts
Max. height diff. UIs = 30 mts
Max. EER/IEER “K” = 15.5 / 22.1
Max. EER/IEER “L” = 14.8 / 28.1
Y-Series – “K” “ L”
Heat-Pump
Up to 360MBH (30 Tons)
Up to 50 indoor units
Max. 90 mts from first derivation
Combination IUs up to 130%
Max. pipe length = 1000 mts
Max. height diff. UIs = 30 mts
Max. EER/IEER “K” = 14.2 / 21.3
Max. EER/IEER “L” = 16.4 / 28.1
S-Series “K”
Heat-Pump
3, 4 y 5 Tons
Up to 12 indoor units
Max. 30 mts from first derivation
Combination UIs up to 130%
Total piping length = 300 mts
Max. height diff. UIs = 15 mts
Max. EER/IEER “L” = 14.2 / 21.0

## Slide 5: Portfolio de Produto
5
5
5
PLFY-VLMD
Ceiling Cassette (2-way)
Only
Only
Nn UL Solamente
*Todas las unidades interiores existen en versión UL y No-UL, a excepción de las mencionadas. Todos los controles son UL.
Sin Ducto 6-48 Mbh
Ductado 6-96 Mbh

## Slide 6: Caracteristicas Claves
Se puden conectar hasta 50 unidades
Modulos disponibles hasta 188 MBH (~16 Toneladas) con capacidades en modulos combinados de 563 MBH (~47 Toneladas).
Tratamiento anticorusivo Blue Fin disponible en toda las unidades.
Operacion garantizada hasta 125.6oF (52oC) con 100% refrigeracion.
Uso efectivo del espacion con una de las dimensiones mas pequenas y peso mas liviano.
Garntia standard de 7 anos en compresor y 1 ano en partes con garantia extendida de 10 anos.
Unico sistema acumulador y separador de aceite de alta eficiencia
Diametro mas pequeno en la industria (hasta un 10% de reduccion en costo).
Puede operar a 4% de capacidad con rendimiento guarantizado.
Usa derivaciones “T” en vez de derivacion “Y” que reduce el costo de instalacion.
El unico sistema de Recobro Energetico de 2 tuberias en vez de 3 tuberias en LAR.
Todo los controladores individuales pueden operar hasta 16 unidades interiores.
Sistema certificado de aporcionamiento de energia.
Integrated Centralized Control Web puede controlar hasta 2000 unidades
Programas de selección de alto rendimiento que incluyen actualizaciones en línea y capacidades para compartir, acceso instantáneo a catálogos, presentaciones, archivos REVIT y AutoCAD
Herramientas de Mantenimiento y Solucion de problemas avanzada.

## Slide 7: Caracteristicas Claves
Todas las demás compañías de HVAC tienen separadores y acumuladores de aceite muy pobres en sus unidades exteriores, lo que generalmente lleva a una migración de aceite de hasta el 90% en promedio, lo que hace que tengan que instalar un tercer tubo para la línea de gas caliente.
Sin embargo, Mitsubishi agrega un separador y acumulador de aceite a sus unidades exteriores, lo que nos permite no tener que agregar un tercer tubo para la recuperación de calor, en lugar de eso, se usa un controlador BC = menos tubería, menos conexiones, menos costos de instalación.
EL UNICO SISTEMA DE 2 TUBERIA DE RECOBRO ENERGETICO!
Notes: The problem with having very poor oil separators and accumulators and adding that extra heating gas line for the oil recovery cycle, this causes zone-temperature drift during recovery cycles and affects the energy efficiency of the unit especially at capacities less than 75% which is where most units operate 98% of the time.
Since in the Mitsubishi model only 6% of oil migration occurs they do not require regular oil recovery cycles to return the oil. Also with less refrigerant volumes and velocities during mode change over, oil recovery is minimized. All this allows for our units to operate more efficiently at lower capacities than any other system and for some outdoor units to even run efficiently at 6% capacity.
BC Controller functions
Separates refrigerant into gas and liquid
Ensures units in heating receive superheated gas
Ensures units in cooling receive sub-cooled liquid

## Slide 8: Caracteristicas Claves.
Otro gran beneficio es que, si una unidad interior falla debido a algún motivo, el sistema continuará funcionando sin tiempo de inactividad.
¡El sistema puede funcionar eficientemente al 4% de su capacidad! ¡Algo que los competidores NO PUEDEN HACER!
Un máximo de 6% de migración de aceite ...
Notes: The problem with having very poor oil separators and accumulators and adding that extra heating gas line for the oil recovery cycle, this causes zone-temperature drift during recovery cycles and affects the energy efficiency of the unit especially at capacities less than 75% which is where most units operate 98% of the time.
Since in the Mitsubishi model only 6% of oil migration occurs they do not require regular oil recovery cycles to return the oil. Also with less refrigerant volumes and velocities during mode change over, oil recovery is minimized. All this allows for our units to operate more efficiently at lower capacities than any other system and for some outdoor units to even run efficiently at 6% capacity.
BC Controller functions
Separates refrigerant into gas and liquid
Ensures units in heating receive superheated gas
Ensures units in cooling receive sub-cooled liquid

## Slide 9: Caracteristica Claves
Calculacion de tuberia para un sistema de 32 HP
 |  |  |  |  |  | Total Length (m) |  |  |  | 
Pipe Size (inch) | Pipe Size (mm) | Pipe Type | Weight per meter | Cost per kg (BRL) | Cost per meter (BRL) | Mitsubishi UL | TVR LX | LG Multi V IV | TVR Select | Mitsubishi Non-UL
3/8 | 9,52 | Flexible | 0,195 | 42,9 | 8,4 |  |  | 160 | 160 | 80
1/2 | 12,7 | Flexible | 0,266 | 42,9 | 11,4 | 240 | 240 | 80 |  | 160
5/8 | 15,87 | Flexible | 0,337 | 42,9 | 14,5 | 200 |  | 160 | 240 | 200
3/4 | 19,05 | Flexible | 0,408 | 42,9 | 17,5 | 30 | 200 | 40 | 40 | 30
7/8 | 22,22 | Rigid | 0,478 | 44,9 | 21,5 | 80 | 30 | 30 | 30 | 80
1 | 25,4 | Rigid | 0,549 | 44,9 | 24,7 |  | 80 | 80 | 80 | 
1 1/8 | 28,57 | Rigid | 0,620 | 44,9 | 27,8 | 40 |  |  |  | 40
1 1/4 | 31,75 | Rigid | 0,691 | 44,9 | 31,0 |  | 42 | 40 | 40 | 
1 1/2 | 38,1 | Rigid | 0,833 | 44,9 | 37,4 |  | 30 | 30 |  | 
1 5/8 | 41,27 | Rigid | 0,904 | 44,9 | 40,6 | 30 |  |  | 30 | 30
Piping Cost |  |  |  |  |  | 10203 | 11280 | 10244 | 10583 | 9960
Inst. Cost Red. |  |  |  |  |  | 2% | 12% | 3% | 6% | Base
Puede haber un ahorro de mas de 10% ….

## Slide 10: Caracteristicas Claves
Chart: IEER
| 72 | 96 | 120 | 144 | 168 | 192
SAMSUNG | 22.5 | 23 | 23 | 21.6 | 20.8 | 21
DAIKIN | 20.7 | 22.5 | 22 | 22.6 | 19.8
LG | 23.5 | 25 | 23 | 22.5 | 19.6
Mitsubishi Electric "L" Gen | 23.1 | 23.1 | 21.9 | 21.2 | 18.7
Chart: IEER
| 192 | 216 | 240 | 264 | 288 | 312 | 336 | 360
SAMSUNG | 20.5 | 20.1 | 19.6 | 21.6 | 20.1 | 19.4 | 18.9
DAIKIN | 21.2 | 21.1 | 20.9 | 19.6 | 19.6 | 18.8 | 18.5 | 18.5
LG | 22.9 | 22.1 | 20 | 21.4 | 19.5 | 21 | 20.5 | 21.2
Mitsubishi Electric "L" Gen | 21.1 | 21 | 20.8 | 21.1 | 20.4 | 20.3 | 20.3 | 20.1
Sistemas Modulares tienen mejores eficiencias.

## Slide 11: Caracteristicas Claves
Fabricante VRF Mini | 27,3 MBH |  | 35,8 MBH |  | 38,2 ~ 42,7 MBH |  | 47,8 MBH |  | 52,9 MBH | 
 | Noise Level | EER (W/W) | Noise Level | EER (W/W) | Noise Level | EER (W/W) | Noise Level | EER (W/W) | Noise Level | EER (W/W)
TVR Mini | - | - | 57 | 3,92 | 57 | 3,69 | 57 | 3,54 | 57 | 3,43
S-Series | - | - | - | - | 49 | 4,48 | 50 | 4,05 | 51 | 3,43
Mini Multi V | - | - | - | - | 50 | 3,39 | 52 | 3,70 | 52 | 3,71
Serie S | 54 | 3,81 | - | - | 55 | 3,70 | 55 | 3,46 | 55 | 3,31
Mitsubishi tiene los mejores productos en esta categoria.
Nivel de sonido mas bajo y eficiencia mas alta.
Specification

## Slide 12: Caracteristicas Claves
High-Wall 5,8 ~ 38,2 MBH | Fancoil low, mid, high 5,8 ~ 76,4 MBH | 4-Way Cassete standard and compact 5,8 ~48 MBH
1-Way cassette 7,5 ~ 15,4 MBH | 2-way cassette 7,5 ~ 48 MBH | Ceiling 15,4 ~48 MBH
Console 7,5 ~ 24 MBH | AHU or LEV kit AHU: 12 ~ 54 MBH LEV kit: 4,8 ~ 240 MBH | Hydronic heat exchanger R2 Series, 36 ~ 72 MBH | Energy recovery ventilator Lossnay 500 ~ 2000 m3/h
3D I-See sensor
As low as 29 dB(A)
As low as 27 dB(A)
As low as 29 dB(A)
As low as 22 dB(A)
Opt. MERV 8 hasta 13 filters
Best enthalpy efficiency
Specification
Specification
Specification
Specification
Specification
Specification
Specification
Specification
Specification

## Slide 13: Caracteristicas Claves
Company | Range of operation in Cooling
Mitsubishi – Y-Series | -5 ~ 52 C
Daikin - VRV IV | -5 ~ 43 C
Samsung – DMV S | -5 ~ 49 C
LG – Multi V IV | -5 ~ 43C
Los dias mas calientes no son un problema…

## Slide 14: Caracteristicas Claves
Company | Warranty
Mitsubishi | Standard 7 years compressor 1 year parts Extended 10 years compressor 10 years part
Daikin | 5 years compressor 2 years parts
Samsung | 5 years compressor 1 year parts
LG | Standard 5 years compressor 2 year parts
Calidad con Responsibilidad…

## Slide 15: Caracteristicas Claves
3D i-See sensor se usa para determinar la ocupacion
OperacionAuto-Off
Draft-less Mode – Individual automatic louver direction
Cassettes Nuevos
  UL
    PLFY-EP**NEMU-E
    PLFY-P**NFMU-E
  Non-UL
    Optional
3D i-See Sensor

## Slide 16: Caracteristicas Claves
Mucho mas que un termostato tipico…
Built-in Sensors
  Occupancy
  Temperature
  Humidity
  Brightness
Touch Screen
Weekly Schedule (with Mode)
Timed Override & Permanent hold of schedules
Dual set point with extended temp range
Energy saving function (occupancy based control)
General equipment monitoring (requires AHC)
Displays room name
ME Style (M-NET addressable)
PAR-U01MEDU-K
SMART ME
Notes: Additional Features:
  Grouping configuration (up to 16 indoor units and one AHC in a group)
  Connected system search function
  Lossnay® interlock setting
  Screen cleaning lock out
  Screen calibration
  Offsets for Temperature and Humidity sensor displays
  Occupancy and Brightness sensor calibration
  Color Indicator On/Off and Customization
  Indoor unit function settings
  Extended set temperature range (dependent on connected system)
  Passwords
    9999 Service (Default)
    0000 User (Default)

## Slide 17: Caracteristicas Claves
Mucho mas que un termostato tipico…
Occupancy Sensor Detectable angle
Unoccupied settings
Funccion Ahorro Energetico
・Horizontal
32.8ft
(10m)
16.4ft
(5m)
16.4ft
(5m)
32.8ft
(10m)
3.9ft(1.2m)
or
4.9ft(1.5m)
・Vertical
New ME R/C
Upper：11.2°
Lower：19.8°
32.8ft
(10m)
31°
Notes: Occupied: Returns to normal operation
Unoccupied (pick one):
  Turn IDU Off
  Change Mode to SETBACK
  Offset the set temperature
  Change Fan Speed to Low
  Force IDU into Thermo-off
Schedule “Active” times for Energy Savings and combine with brightness sensor to help determine occupancy

## Slide 18: Caracteristicas Claves
Kumo Cloud
Compatible with CITY MULTI and M and P-Series units
Smaller unit measuring 2.9” x 1.8” x 0.7”
Velcro mounting strip for easier mounting and removing
Easy to connect the device to your router using the kumo cloud app
App compatible software platforms:
— Apple iOS 8.0 or later
— Android 4.1 or later
— Fire OS 4.1 or later
Intuitive settings for simplified use:
—Group units together
—Organize groups into sites
—Batch command units
Error and filter status pop-up
Controla su sistema remotamente….!

## Slide 19: Kumo Cloud

## Slide 20: Caracteristicas Clave
Kumo Cloud y integracion Alexa
“Alexa, set living room to auto.”
“Alexa, what is living room set to?”
“Alexa, what is the temperature in the kitchen?”
“Alexa, increase bedroom by 4 degrees.”
“Alexa, set downstairs to cool”
“Alexa, set dining room to heat.”
Controla su sistema con Alexa!

## Slide 21: Caracteristicas Claves
Features
Full color, touch screen display
Bluetooth app for users & installer
Can display customer logo
Scheduling ability
Controls 1-16 indoor units
MA style wiring
  Wires directly to indoor unit
  Reduced MA wire length
    70m (229’) because of power consumption
    NOT standard 656 ft. wire length
  No Sub MA remote
PAR-CT01MAU-SB
Alguien dijo Bluetooth?
Control Bluetooth de 33’

## Slide 22: Caracteristicas Clave
Thermostat Control
PAC-US444-CN-1
Thermostat Interface
M&P or CITY MULTI
One interface per indoor unit
Modes:
  Cool, Heat, Fan, and Off
Fan Speed Control
  High, Medium, Low
Nest? ecobee? Sin problema!
CN-105

## Slide 23: Key features and Sweet Spots!
Procon Interface- PAC-UKPRC001-CN1-1
1:1 gateway for a single indoor unit
Configurable for BACnet or Modbus
Intended to add a stand-alone unit into an existing BAS
Supported for use with a central controller, unlike kumo cloud
Some applications:
  10 or fewer units to integrate into a 3rd party BMS
    Spot cooling in commercial buildings
    IDF closets, Guard Houses, Kitchens
  National companies with distributed locations
    Retail and fast food
BMS para solamente 1 unidad de A/C? Lo podemos hacer!
Notes: Procon PAC-UKPRC001-CN1
  1-to-1 connection for 1 indoor unit
  Configurable for BACnet or Modbus
  Used for an independent unit within an existing BAS
  Compatible with central controller
  P-series data closet control and monitoring

## Slide 24: Caracteristica Clave
MAC-333IF-E - M-Series Control Adapter
M-NET  Centralized Controller, BACnet, or LonWorks
To send status output to BMS
As a centralized On/Off control for indoor units or restricted operations
To check whether a unit in fault
So M-Series units communicate with our CITY MULTI Controls Network via M-Net
For back-up heating
Wired or Simple MA remote
  **not required to add Simple MA on SEZ/SLZ/MVZ
Tambien quiero integrar mi sistema mini split… Claro que Si!
CN-105
Notes: MAC-333IF
  Interface to allow a standalone m-series residential minisplit to communicate with city multi controls.
  Has two outputs for :
    Equipment status and error
    Humidifier control
  Provides an input to allow remote on/off control of IDU
Packaged Handheld Wireless Remote (default option)
MHK1 Wall Mounted Wireless Remote
  Compatible with Honeywell RedLink Internet Gateway for remote access using mobile apps or internet browser
MAC-333IF-E Control Adapter connected to each INDOOR unit
  Allows for connection to M-NET
    Requires 12VDC power supply if using MHK1 while connected to M-NET
    Monitor and control from central controller
    Tie into BACnet or LonWorks system through AE-200/50/EW-50 or LMAP04U
  Allows for dry contact control
    Requires 12VDC power supply
    Remote Start/Stop
    Error Status
    Humidifier Enable
    Supplemental Heat Enable
  Allows for control by PAC-YT53CRAU Simple MA Remote

## Slide 25: Caracteristicas Clave
Connectores 52, 51, and 32 se pueden usar como entradas y salidas libres.
Controladas usando progrmacion interconectada en el AE-200
SW1-9 y SW1-10 deben estar activados por IDU
Control de salida pulsada, bloqueo del ventilador, amortiguador de aislamiento, interruptor de ventana, etc.
Example:

## Slide 26: Caracteristicas Clave
10.4” LCD color touch screen controller
Control of temperature, fan speed and airflow options at the touch of a button.
Comprehensive energy consumption monitoring and comparisons with the previous year's power consumption.
Control up to 200 units by using three AE50 expansion controllers.
Floor layout is displayed on the 10.4-inch LCD touch panel
PC Monitoring
PC Scheduling
Online Error Email
Online Maintenance Tool
Interlock Function
Optional Software Package
  Tenant Billing
  Personal Web Browser
AE-200
Controlador Centralizado de Ultima Generacion!!!!
Capable to connect to existing building’s LAN
Controls Indoor units, Lossnay, DOAS, PWFY, DIDO, AI, M-Series and P-Series
Compatible with BACnet and LONWorks Interfaces
Compatible with SW-Bacnet, SW-Charge, SW-P-web

## Slide 27: Caracteristicas Clave
Controls various centralized controllers
With the ICCW, now you can control up to 100 AE-200’s
Capable of managing up to 2000 indoor units from one IP
Floor layout
Groups
Measurement / ACH status
Energy use status
Peak cut
Unit error log
Communication error log
Filter sign
Scheduling: today, weekly, annual
Send mail log
Outdoor Unit status
Integrated Centralized Control Web (ICCW)
Un edificio o muchos … dejanos ensenarle como…
Notes: ICCW (integrated centralized control web) is free. (see attached presentation on ICCW)
  Scheduling
  System errors
  Screen display settings
  Energy consumption (w/o meter) daily, annual
  Condenser status
  OU/IU free contact status CN32, CN51, CN52

## Slide 28: Caracteristica Clave
Initial Settings Tool
Ahorros, comfort, integracion…
Notes: Several functions can be used via the initial settings browser (see attached presentation)
  Peak Cut – where equipment reaching a peak, turn off equipment or change set point
  Set Temperature range limit or limit ranges for user
  Night mode – used when local codes restrict dB levels. You can reduce capacity of external equipment and thus dB to not exceed 60%-70%
  System changeover
  External temperature interlock
  Night setback control – turn off IDU’s to let them reach a cooler/hotter temperature depending on system setting. They will turn back on when they get to a certain limit that you’ve indicated. This changes your schedule due to last command wins.
  Interlock control – lets you install motion detectors, ventilators, door switches. Let’s you control various aspects of the building.

## Slide 29: Caracteristicas Clave
AE-200
Collects energy data
Charge Calc Tool
Prints spreadsheet
Expansion Ctlr
Hosts M-NET network
PI Ctlr
Collects kWh Pulses
kWh Pulse Meter
Measures ODU kWh use
Tenant A
IDU Conditions set by tenant
Tenant B
IDU Conditions set by tenant
Ethernet Connection
M-NET Connection
ODU Electrical Supply
kWh Pulse Output
Configuracion de Site para Aporcionamiento de Energia
Contabilidad de inquilino conduce a la reduccion de los costos energeticos.

## Slide 30: Recursos
Su punto de acceso principal para obtener información: www.mylinkdrive.com
Envíos, especificaciones, AutoCAD, REVIT, manuales de ingeniería y mucho más.
Otro buen recurso: www.mitsubishipro.com
Casos de estudio, guías de diseño, libros blancos, información de formación.
Almuerza y ​​aprende - ¡Habla con las personas que diseñan los sistemas! ¡Cuéntales sobre los puntos dulces! PPT disponible en el sitio de SharePoint sin conductos.
Las herramientas de selección, que estén disponibles!
Diamond System Builder (DSB) - UL y la nueva herramienta de diseño - No UL.
Venta financiera, el primer costo no es la única variable en la ecuación.